## Slide 1
Rebuilding the Data Foundation
Rain or Pumps? Attributing India’s Groundwater Decline District by District
What changed in the data, why we changed it, and how your feedback was applied
TEAM
Kakara Siva Kumar
Rainchwar Parth
Vipul Aggarwal
MENTOR
Sudharshan Deshmukh
BITS Pilani | PGCP in AI and Machine Learning | Group 18
Notes: One line up front: we went back to the raw archive, and the file we had been using turned out to be filtered in a way that hides decline.

## Slide 2
What changed, in one view
Same two sources. A different foundation built from them.
Before
Now
Starting point
The published 2,759-well file
The raw archive, 32,299 wells
Bad readings
Removed upstream, unseen by us
Flagged and kept: 94.7% valid
Well location
District name printed in the file
Placed inside a district outline by coordinates
Specific yield
Guessed from a state median
Read from the hydrogeological map
Time alignment
Monthly rainfall totals
Four seasons cut at the readings
Rain at a well
Nearest grid node
Four surrounding nodes, distance weighted
District rainfall
Cells the district’s wells sat in
Every cell it covers, weighted by area
What we predict
The water level itself
The change in level since the previous reading
Wells we can model
2,759
11,455 (the 2,759 kept as a control arm)
16
cleaned tables
251
columns documented
145
automated tests
694,253
training rows ready
Notes: Nothing here was hand edited. Every table is rebuilt from the raw files by code.

## Slide 3
Why we rebuilt: the file we had was already filtered
And the filter removed the wells that were getting worse
1
How 32,299 wells became 2,759
Step
Wells left
Raw archive
32,299
Has any reading 2000–22
29,537
No negative reading anywhere
28,612
At least 2 readings in every year
2,876
No value repeating 3+ times
2,759
Replaying this cascade reproduces the published 2,759 exactly, which is how we know where the rest went.
2
The fourth rule is the problem
It alone removes 25,736 wells, more than every other rule combined
It tests completeness, not quality: a well with 91 of its 92 readings is discarded if one single year holds only one of them
The wells it removes are not a random sample. They are more likely to be deepening
The consequence, measured
Wells deepening
Mean trend
Published 2,759 wells
38%
−0.0345 m/yr
The 6,050 wells added back
46%
+0.0217 m/yr
The published set understates the decline.
Notes: This is the headline. Say it plainly: the dataset everyone uses is biased toward the steadier wells, so it makes the problem look smaller than it is.

## Slide 4
Flag, do not drop
Every reading is kept. Selection happens once, at the very end.
1
What is wrong, named per reading
Flag
Readings
Wells
Water deeper than the well
26,257
2,755
Three or more identical in a row
22,448
1,950
Suspect zeros (missing as 0)
13,488
753
Outlier vs its own season
9,587
7,485
Water above ground
1,429
925
Valid
1,065,392
94.7%
Outliers are measured against each well’s own seasonal pattern, not its raw level, so a genuine long decline is never flagged as an anomaly.
2
Two views, not one cut
View
Wells
States
Strict (control)
2,759
21
Modelling
8,629
22
Training table
11,455
27
The training table needs three of four campaigns rather than all four, which keeps Kerala, Assam, West Bengal and Odisha.
3
Bad data is concentrated
Telangana: 16.7% suspect zeros and 17.9% below-bottom readings
Nationally for dug wells: 0.2% and 0.8%
Bore wells and piezometers carry nearly all of it
Notes: The point of flagging rather than dropping is that the decision stays visible and reversible.

## Slide 5
Fixing what the source file gets wrong
Each fix is checked against independent evidence, not assumed
1
Where the well is
610 district names mix spellings, renames and boundary vintages, so names cannot be joined reliably
Every well is now placed inside the district outline its coordinates fall in (724 post-2020 outlines)
The file label agrees for 82.5%; the rest are renames and splits
489 wells are filed in the wrong state. Their levels track neighbours at their coordinates at 0.39, against 0.17 for the labelled district, so the label is what is wrong
2
Specific yield
Needed to turn a level change into millimetres of water. The raw file has none
The hydrogeological map sits in the same archive and reproduces the published values for 100% of wells tested
Our earlier state-median guesses landed in the wrong class for 8,996 wells, and were more than 1.5x off for 75% of those
Every well now reads its value from the map
3
Aquifer and well type
Blank for 13,312 wells, so those wells could not be grouped by how the aquifer behaves
99.6% of dug wells that do carry a type are unconfined, so blank dug wells are inferred Unconfined (6,308)
Bore wells, tube wells and piezometers are too mixed to infer, so they stay Unknown
The original values are kept alongside, and the source of every value is recorded
Notes: Theme of the slide: nothing was guessed where evidence existed, and where we did infer, the rule is stated and the original kept.

## Slide 6
Putting rain and wells on one clock
Rain is daily, levels are quarterly. They only meet once rain is summed between readings.
1
Four seasons, cut at the readings
Season
From – to
Days
Nov–Jan
Nov 16 – Jan 15
61
Jan–May
Jan 16 – May 15
120
May–Aug
May 16 – Aug 15
92
Aug–Nov
Aug 16 – Nov 15
92
Calendar quarters would split the monsoon across the August reading. Season rain is summed from the daily grid and matches the raw files to 0.0001 mm.
2
A level is a stock, rain is a flow
Rain in a season does not explain the water level. It explains the change in level over that season
Specific yield converts that change into millimetres of water, so rain in and water stored share one unit
A missing reading is bridged to the last valid one, never filled in. 88% of changes come from the season immediately before
3
The physics comes out right, which is the check that it works
Season
Change in level
Rain
Share stored
Jan–May (dry)
falls 1.42 m
39 mm
—
May–Aug (monsoon)
rises 1.94 m
482 mm
11.6%
Aug–Nov (late monsoon)
falls 0.15 m
359 mm
≈ 0
11.6% sits inside CGWB’s own published infiltration range of 8–15%, from an independent source we never fitted to.
Notes: This is the strongest validation in the rebuild: an independent authority publishes 8 to 15 percent and our number lands at 11.6.

## Slide 7
Your feedback, and what we did with it
All four are now in the plan. One changed shape, and the reason is measured.
DONE
Use a non-linear distance function for the many-to-one mapping
Built inverse-distance (power 2) and bicubic alongside bilinear, and compared them by hiding grid points and predicting them back. Bilinear won: 17.7% monthly error against 25.6% for the nearest point.
ADAPTED
Take the centroid of the group and use it as the well location
Not adopted for grouping wells: two wells in one cell already differ by 0.90 m while the signal is 0.48–0.95 m, so averaging would erase real variation, and distance weighting versus a plain mean differs by only 0.038 m at this density. Applied instead to the 2,999 wells whose coordinates were recorded rounded, where the position genuinely is uncertain.
ADOPTED
A recurrent model reading a 30-day sequence, fed forward
Adopted, with the output moved. Your 30-day rainfall version was tested and it confirmed the problem you were probing: a model reading 30 days of rain falls back to the calendar average within a week, because no gauge exists at a well to train the rainfall output against. So the recurrent model now reads the 52-week rain sequence at a well and predicts the change in its water level, which has 23 years of real labels behind it.
DONE
Pick two architectures, train both, compare
Your own phrase is the split we used. Architecture A, many inputs and one output: ridge and LightGBM on 25 features. Architecture B, recurrent: the LSTM on the weekly sequence. Identical rows and splits, both scored against two no-skill baselines.
Notes: Lead with the recurrent row. He asked for a sequence model, we tested his exact version, it failed for a reason we can name, and the architecture is now in the plan pointed at a target that has labels. That is the respectful version of disagreeing.

## Slide 8
How the two architectures will be built and compared
Specified on identical rows and splits, so the comparison means something
1
The question
Given the rain that fell at a well, how far should its water level have moved this season
Target: the change in level since the previous reading, in metres
Never inputs: past water level, year, coordinates, district or state, because each carries the pumping history we are trying to measure
2
The models
Baselines: predict no change, and each well’s own average for that season. Every model must beat both
A, many inputs one output: ridge (the linear baseline) and LightGBM on 25 features, with a monotone constraint so more rain can never predict deeper water
B, recurrent: LSTM or GRU over 52 weekly rain totals, with well properties joining after the recurrent layer
3
How they are judged
RMSE, MAE and skill against the baselines, reported per season and never pooled into one number
Two hold-outs: unseen years, and whole unseen districts across five folds
Monotonicity: scaling rain 0.8x to 1.2x must never make predicted water deeper
Sanity: predicted May-Aug storage should land near CGWB’s 8–15% infiltration range
Split once, by year, and the test years stay closed until the end
Train
2000–2014
489,707 rows
Validate
2015–2017
85,250 rows
Test
2018–2022
119,296 rows
Plus
5 district folds
whole unseen districts
Notes: If he pushes on why the recurrent model might not win: if B cannot beat A, it means timing inside a season adds little beyond the totals, and that is itself a reportable result.

## Slide 9
Where it stands
Closed this week
The data layer is rebuilt from the raw archive and nothing is hand edited
Location, specific yield and aquifer type are all evidence based
Rain and levels share one clock, validated against CGWB’s own infiltration range
145 automated tests, 251 columns documented from the tables themselves
Still open
Rain explains a modest share: season rain correlates −0.08 to −0.16 with the change. The unexplained part is what the project measures
CGWB’s Safe / Critical / Over-exploited categories are not obtained yet, and the ranking needs them to be validated
Specific yield is a five-class map value, so storage in millimetres is approximate; the change in metres does not depend on it
Readings carry a month but no day, so season edges are uncertain by about two weeks
What we need from you
Confirm the training table at 11,455 wells, with the published 2,759 kept as the control arm
A view on whether the expanded, less filtered set changes what we can responsibly claim about decline
Help sourcing the CGWB category dataset, which is the only external check the ranking has
Every number on these slides is regenerated by script from the raw files. Nothing was typed in by hand.
Notes: End on the ask, so the meeting closes with a decision rather than a summary.