## Slide 1
Rain or Pumps?
Attributing India's Groundwater Decline District by District
TEAM
Kakara Siva Kumar
Rainchwar Parth
Vipul Aggarwal
MENTOR
Sudharshan Deshmukh
Industry mentor, weekly review
BITS Pilani | PGCP in AI and Machine Learning | Capstone Project
Notes: Introduce the problem in one line: separate the effect of rainfall variability from human extraction in explaining district level groundwater decline.

## Slide 2
Two datasets, two different shapes
Point measurements on one side, a continuous grid on the other
1
CGWB groundwater levels
Central Ground Water Board, 2000 to 2022
2,759 quality controlled monitoring wells
Four campaigns a year: January, May, August, November
92 readings per well, one column each in the raw file
Depth to water plus specific yield per well
figshare, CC BY 4.0, doi 10.6084/m9.figshare.29293877
2
IMD gridded rainfall
India Meteorological Department, 1998 to 2022
0.25 degree grid, 129 by 135 cells, about 27 km per cell
Daily rainfall, one NetCDF file per year
25 files downloaded; 1998 and 1999 carry the lag windows
Gap free, so rainfall features have no missing values
Open access, imdpune.gov.in
Target variable gwl_mbgl groundwater level in metres below ground level
Measured downward from the surface, so a larger number means deeper water. A groundwater decline appears as an increase.
Notes: Stress the direction of the target. Bigger means deeper means worse. Every rainfall correlation is therefore negative.

## Slide 3
Mapping CGWB wells to IMD rainfall
The two files share no key, so the join is built on geography and time
The problem: both files carry latitude and longitude, but IMD coordinates are a fixed 0.25 degree lattice while wells sit at arbitrary points. Only 3 of 2,759 wells match an IMD coordinate exactly.
1
Spatial join
Each well is snapped to its nearest grid node, giving a cell_id key. 2,759 wells fall into 1,547 cells, an average of 10.2 km from the well to the cell centre.
2
Temporal join
Daily rainfall is aggregated to monthly totals and rainy day counts, then joined on cell and the month of the reading. Only trailing history is attached.
3
District roll up
Wells aggregate using CGWB's own district column, so no district name is ever matched across datasets and boundary changes cannot corrupt the join.
464,100
cell months of rainfall
253,828
well season observations
22,715
rows in the final data set
272
districts retained
Notes: The punchline: a naive merge on latitude and longitude would have matched 3 wells and silently dropped 2,756.

## Slide 4
Cleanup, feature engineering, correlation
Everything between the raw files and a modelling table
Data cleanup
Station Code is corrupted by scientific notation, only 182 unique codes for 2,759 wells, so a minted well_id replaces it
13.6 percent of readings missing, concentrated in May at about 30 percent because dug wells run dry before the monsoon
The target is never imputed. Imputing levels would fabricate the signal later read as extraction
Districts need at least three wells, keeping 272 of 365
Feature engineering
Ground rule: nothing the model could not have known on the day of the reading
How much rain fell recently, as totals over the last 3, 6, 12, 24 and 36 months. Shallow wells react within months, while deep storage takes years
How the rain arrived, as a count of rainy days, because many light showers soak in while one cloudburst mostly runs off
A dry year or simply a dry place, by measuring rainfall against that location own normal so an arid district is not judged by a wet district standard
Last year level at the same well, because an aquifer remembers where it started
Correlation
More rain means a shallower water table. Since the target is a depth, that shows up as a negative correlation, strongest over the last three to six months
Comparing districts with each other mixes two stories: wet regions simply have shallower water, and wet years lift the water. Looking inside each district separates them, and 96 percent then behave as the physics predicts
Last year level predicts this year almost perfectly, but it already carries last year pumping inside it. Using it would hide the very thing we are trying to measure, so it stays out of the attribution model
Notes: Correlation is not causation: the residual design plus validation against CGWB stress categories is what carries the attribution claim.

## Slide 5
Early baseline regression strategy
Model the rainfall expected level, then read what rainfall cannot explain
Rainfall history
Rainfall expected level
Observed minus expected
Persistent gap = extraction pressure
Models and validation
Model 1: regularised linear regression, Ridge or ElasticNet, on rainfall features only. This is the counterfactual and it stays interpretable in metres
Model 2: gradient boosting, XGBoost or LightGBM, for the non linear rainfall to level response
Two variants answer two questions. Rainfall only is for attribution, plus lagged level is for forecasting, and the two are never mixed
Validation: GroupKFold by district for spatial generalisation and blocked by year for temporal, with RMSE, MAE and R squared reported per season
Notes: The residual is only read as extraction when it is systematic across several years, never from a single year gap.

## Slide 6
Future scope
Where the remaining weeks extend the baseline
Classification layer
Predict the CGWB safe, semi critical, critical and over exploited categories to validate the ranking. Class weights compared against SMOTE, scored on PR AUC rather than accuracy.
Unsupervised learning
Cluster districts by their rainfall response signature using K Means and PCA, separating structural decline from recoverable decline.
Deep learning
A multi layer perceptron benchmarked against gradient boosting on identical splits, and a sequence model over the level history if time allows.
Exogenous rainfall drivers
SARIMAX with ENSO and Indian Ocean Dipole indices, the only route to genuine monsoon forecast skill beyond climatology.
Serving layer
FastAPI endpoints for prediction, what if rainfall scenarios and district ranking, so the models are callable rather than notebook bound.
LLM interface
A LangGraph agent calling those endpoints, with retrieval over CGWB assessment reports, producing grounded district briefs. This carries the text mining component.
Known limitation being addressed: a district mean shifts as wells drop in and out of reporting, so well level models with well effects are the planned cross check.
Notes: Close by naming the single decision needed from the mentor this week: confirm the dataset grain, district season against district year.