## Slide 1
WEEK 5 REVIEW · 3 OCTOBER 2026
Two sequence models, one answer
BiLSTM and Transformer on identical data, and what the comparison actually shows
216,455
rows, 2,759 wells
delta_h_m
target, + = level fell
33
tabular features
104
weeks of rain per row
Both models read the same rows, the same split and the same leakage guard. Any difference is the architecture.
Kakara Siva Kumar · Rainchwar Parth · Vipul Aggarwal Mentor: Sudharshan Deshmukh
Notes: Train 2000-14, validate 2015-17, test 2018-22, blocked by year. Normals from training years only. Both pipelines abort if a past water level, the year, coordinates, district, state or well id appears as a feature.

## Slide 2
Headline: a three-way tie
Chart: Validation 2015-2017, R² (higher is better)
| Predict zero | Ridge | Season mean | Transformer | BiLSTM | LightGBM
Validation R² | 0 | 0.209 | 0.271 | 0.418 | 0.419 | 0.435
What we claim
Two different sequence architectures, given raw weekly rainfall, both recover gradient boosting on hand-engineered rain windows.
The transformer made that claim once. The BiLSTM makes it independently.
What we do not claim
That any model won. All three sit within 0.016 m of MAE of each other, from a single seed. None of those gaps is a result.
Repeat seeds are next step one.
Transformer 176,817 parameters · BiLSTM 183,122, sized deliberately to match so capacity cannot explain a difference
Notes: Read the ladder, not the top number: zero gives 0.00, the seasonal average 0.27, the models 0.42. LightGBM reads 0.435 on Parth machine against 0.431 on mine, same code, different library version.

## Slide 3
Held-out years and held-out districts
TEST 2018-2022, NEVER TOUCHED UNTIL THE END
Model | MAE (m) | RMSE (m) | R²
BiLSTM | 1.449 | 2.298 | 0.441
Transformer | 1.457 | 2.302 | 0.439
FIVE DISTRICT FOLDS, WHOLE DISTRICTS HELD OUT
Fold | BiLSTM MAE | BiLSTM R² | Trf MAE | Trf R²
0 | 1.419 | 0.426 | 1.424 | 0.432
1 | 1.450 | 0.526 | 1.445 | 0.531
2 | 1.452 | 0.497 | 1.445 | 0.508
3 | 1.354 | 0.484 | 1.354 | 0.487
4 | 1.527 | 0.471 | 1.528 | 0.472
Mean | 1.441 | 0.481 | 1.439 | 0.486
The finding worth the slide
Unseen districts are easier than unseen years.
R² is about 0.48 across places the model has never seen, against about 0.42 across years it has never seen. The harder shift is time, not place.
Why that matters here
We are building a district-level product. It has to work in districts with thin monitoring. This says it will.
Both models tie on every single fold. Test scores sit above validation for both, so neither is decaying as it moves forward in time.
Notes: The district-fold run was pending at the last review. It is now done for both models, on the same folds.

## Slide 4
What the rain history alone can do
Strip out every tabular feature and leave only the rainfall sequence. This tests whether rain is carrying the model.
Chart: 
| Transformer 1 rain channel | BiLSTM 1 rain channel | BiLSTM 5 channels | BiLSTM 6 channels
Sequence-only R² | 0.342 | 0.36 | 0.394 | 0.4
Most of the gap is the data, not the architecture
On one identical rain channel the two architectures differ by 0.018. The five extra input channels add 0.035 on top of that.
Both models found the monsoon unaided
Every attention and pooling peak falls in the late monsoon, and the peaks repeat about 52 weeks apart. Neither model was given a monsoon feature.
Why it matters. The more of the explained variance comes from rainfall rather than static well properties, the more honestly the residual reads as extraction pressure. The BiLSTM’s rain history alone recovers 95 percent of its full model; the transformer’s recovers 82 percent.
Notes: The anomaly channel encodes well identity and was the obvious suspect, but removing it costs only 0.006. Fair next step is running the transformer on the same six channels before closing the comparison.

## Slide 5
The problem no fit metric would have shown
Every week of rain on the validation rows was scaled by 0.8 and by 1.2. Less rain should mean a larger fall.
Model | rain × 0.8 | rain × 1.2 | Direction
BiLSTM, 6 channels | +0.012 m | −0.009 m | correct
BiLSTM, no anomaly channel | −0.023 m | +0.018 m | REVERSED
BiLSTM, main data, rain only | −0.007 m | +0.006 m | REVERSED
Two of the three predict a SMALLER fall after a drier two years. That is backwards.
Even the model that moves the right way moves only about 1 cm for a 20 percent change in two years of rain.
What this blocks
The week 7 what-if simulator. "If this district got 20 percent more monsoon rain, would it recover?" is exactly the question these models cannot answer yet.
The two fixes
A monotonic constraint on the rain response, which LightGBM supports directly
A training penalty that pushes the rain response the right way
This check now runs on every candidate model. It is the most useful thing we learned this week.
Notes: Lead with this if time is short. A model can fit well and still have no usable dose-response to its main driver, and the fit metrics are blind to it. Finding this before building the simulator saved real work.

## Slide 6
WHERE WE GO NEXT
Five things, in order
1
Repeat seeds
Three to five runs before any 0.01 m gap goes on a slide
2
Rain-response constraint
A fixed sign on the rain response. The simulator depends on it
3
Transformer on the six channels
Separates channels from architecture in the sequence-only gap
4
The full 694k-row table
Where sequence models may finally beat boosting on data
5
Fit district effects properly
Turns the residual hook into the actual attribution
Residual hook, not the attribution
Junagadh tops both models’ district lists, trained separately. The BiLSTM’s list clusters geographically in Saurashtra and western Madhya Pradesh.
No district effects fitted, no trend estimated, some entries rest on three wells. It shows the chain runs end to end, nothing more.
Items 1 and 2 are blockers
Nothing goes in front of a user until the models have a reliable rain response and the gaps between them survive repeat seeds.
Notes: Items three to five are improvements rather than blockers.